Web Map Tile Service (WMTS)

The WMTS is an OGC standard for distributing tile sets of geospatial data. This is a faster and a more efficient way of distributing data than WMS because with WMTS the tile sets are pre-generated and the client only requests the transmission of the tiles and not their production. A WMS request typically involves both the generation and transmission of the data. A well known example of a non-OGC standard for viewing tiled geospatial data is Google Maps.

In order to display the data at a variety of scales close to what the user might want, the WMTS tile sets are produced at several different scale levels and are made available for the GIS client to request them.

This diagram illustrates the concept of tile sets:

The two types of WMTS interfaces that QGIS supports are via Key-Value-Pairs (KVP) and RESTful. These two interfaces are different and you need to specify them to QGIS differently.

- In order to access a WMTS KVP service, a QGIS user uses the WMS/WMTS interface and adds the string “?SERVICE=WMTS&REQUEST=GetCapabilities” to the URL of the WMTS tile service. An example of this type of address is: http://opencache.statkart.no/gatekeeper/gk/gk.open_wmts?service=WMTS&request=GetCapabilities      	        (the topo2 layer in this WMTS works nicely)						  (Adding this string indicates that a WMTS web service is to be used instead of a WMS service)

- The RESTful WMTS service takes a different form, it is a straightforward URL, the format recommended by the OGC is: {WMTSBaseURL}/1.0.0/WMTSCapabilities.xml this format helps you to recognize that it is a RESTful address. A RESTful WMTS is accessed in QGIS by simply adding its address in the WMS setup in the URL field of the form. An example of this type of address is:			    http://maps.wien.gv.at/basemap/1.0.0/WMTSCapabilities.xml				    which is the address of an Austrian basemap